## Slide 1: Control logic design
Module 6

## Slide 2
The control logic initiates all microoperations in data processor
To execute instructions, the processor must have some means of generating the control signals needed in the proper sequence
Done using sequential circuit whose internal states dictate the control functions of the system
I.e., at any time, state of sequential control initiates a set of microoperations

## Slide 3: Control organization
Hardwired control
  One flip flop per stage method (aka Ring counter controller)
  Sequence register and decoder method (aka counter decoder method)
PLA control
Microprogrammed control

## Slide 4: Hard wired control

## Slide 5: 1. One flip flop per stage
One flip flop set at a time
Single bit propagates under the control of design logic
Each represents a state
Transition: function of
input and present Ti.

## Slide 6: Example[Hardwired control-example1]
Design carried out with 5 steps:
  Problem statement
  Initial equipment configuration
  Algorithm formulation
  Data processor part specification
  Design of control logic
Problem statement: Addition and subtraction of binary fixed point numbers, negative numbers in sign’s 2 complement form

## Slide 7
Equipment configuration:
  Registers
  A,B: numbers to be added/ subtracted stored in these reg
  : sign bits
  E: 1 bit register storing overflow info
  Input signals to control logic
  and : add/subtract operation to be performed
  Output signal
  x : indicates end of operation

## Slide 8
  Data processor part specification

## Slide 10
Algorithm:

## Slide 11
Control state diagram

## Slide 13
Design of hard wired control
  8 states are required as we have seen.
  So 8 D flipflops used with the following input functions(implemented in decision logic)
  At a time, any of the state will be active and corresponding D flipflop will be activated
  The output signals are generated according to the booean function(in table) using OR gate.

## Slide 14: 2. Sequence register and decoder method
Register: to sequence control states
Register decoded to provide one output for each state

## Slide 15: Example[Hardwired control-example2]
Problem statement: To design an arithmetic circuit that multiplies two fixed point binary numbers in sign magnitude representation
Equipment configuration:
  Registers
  B: to store multiplicand, Q-multiplier, A-partial product
  ,: sign bits
  P: counter(no of bits in the multiplier, decremented after formation of each partial product)
  Input signals to control logic
  : operation to be performed
  Output signal
  : rightmost bit in register Q

## Slide 19
Output from control logic:
  T0-indicates that system in initial state
  T1-loads sign to As and k into P
  T2-decrements P,
    If Q=1, L generated- loads A (sum)and E
  T3-Shifts A,Q, clears E

## Slide 20
Design of hard wired control
  2 JK flipflops and 1 2x4 decoder can be used as there are 4 states

## Slide 22: 3. Programmable Logic Array
PLA replaces decoder and decision logic circuits
Internal paths inside PLA are programmed according to program table
Similar to sequence register and decoder method, except that all combinational circuits are implemented with PLA

## Slide 23: PLA basics
The AND and OR gates inside the PLA are initially fabricated with the links (fuses) among them
The specific Boolean functions are implemented in sum of products form by opening appropriate links and leaving the desired connections.

## Slide 25: Example(section 10.7)
Design steps:
Obtain state table for controller
  (No of states determine the number of flipflops for sequence reg)
Connect PLA to sequence register and to input and output variables
  PLA program table obtained from state table

## Slide 26
Consider the example of binary multiplier

## Slide 27
Output from control logic:
  T0-indicates that system in initial state
  T1-loads sign to As and k into P
  T2-decrements P,
    If Q=1, L generated- loads A (sum)and E
  T3-Shifts A,Q, clears E

## Slide 28
G1 and G2 –flipflops(sequence reg)
Input to PLA- value of present state and 3 ext input

## Slide 29: Microprogrammed Control
Control unit initiate a series of sequential steps of microoperations
At any time certain operations are to be initiated and others idle
So represented as series of 1’s and 0’s ->control word
Microprogrammed-> CU whose control variables are stored in memory
Microinstruction
Microprogram
Control memory

## Slide 31: Example(section 10.4)
Problem statement: To design control logic for sign magnitude adder subtractor using microprogram control
State in control memory- address of microinstruction

## Slide 32
Control state diagram

## Slide 37: Control of processor unit

## Slide 38: Example2
Problem: counting no of 1’s in register R1
Algorithm:

## Slide 40: Microprogram sequencer
Microprogram CU control memory
                Next address generator
Address generation part- sequencer
Sequencer provide the following capabilities
  Increments the present address
  Branches to address specified in address field of microinstruction
  Branches to address if specified status bit is 1
  Transfers to new address specified by external source
  Has facility for subroutine calls and return

## Slide 42
Output from CAR- address of control memory
,T have no effect when =00,01,10
Conditional branch operation:
When =11, =0
  If T=1, sequencer branches to BRA(branch address from microinstruction)
  If T=0, increments CAR
Conditional subroutine call:
When =111
  If T=1, CAR+1 pushed to stack,sequencerbranches to BRA
  If T=0, increments CAR
Return from subroutine:
When =01
  Pop stack – branch to address on top of stack

## Slide 44: Microprogrammed CPU organization