## Slide 1: MicroProgramming

## Slide 2: Horizontal Versus Vertical Microcode Schemes
In horizontal microcode, each control signal is represented by a bit in the instruction
  Fewer control store words of more bits per word
In vertical microcode, a set of true control signals is represented by a shorter code
  Vertical code only allows RTs in a step for which there is a vertical instruction code
  Thus vertical code may take more control store words of fewer bits

## Slide 3: Fig 5.25 A Somewhat Vertical Encoding
Scheme would save (16+7) - (4+3) = 16 bits/word in the case illustrated

## Slide 4: Fig 5.26 Completely Horizontal and Vertical Microcoding

## Slide 5: Saving Control Store Bits With Horizontal Microcode
Some control signals cannot possibly be true at the same time
  One and only one ALU function can be selected
  Only one register out gate can be true with a single bus
  Memory read and write cannot be true at the same step
A set of m such signals can be encoded using log2m bits (log2(m+1) to allow for no signal true)
The raw control signals can then be generated by a k to 2k decoder, where 2k ≥ m (or 2k ≥ m+1)
This is a compromise between horizontal and vertical encoding