## Slide 1: Register Transfer Logic

## Slide 2: Register Transfer Logic
Combinational and sequential circuits can be used to create simple digital systems.
These are the low-level building blocks of a digital computer.
Simple digital systems are frequently characterized in terms of
  the registers they contain, and
  the operations that they perform.
Register transfer language
  A symbolic language
  A convenient tool for describing the internal organization of digital computers
  Can also be used to facilitate the design process of digital systems.

## Slide 3
Definition of the (internal) organization of a computer
  Set of registers and their functions
  Microoperations set
  Information stored in registers
  Control signals that initiate the sequence of microoperations (to perform the functions)
The operations on the data in registers are called microoperations.
The functions built into registers are examples of microoperations
  Shift,Load,Clear,Increment…

## Slide 4
Microoperations classified as:
  Register transfer microoperations
  Arithmetic microoperations
  Logic microoperations
  Shift microoperations

## Slide 5: Inter register transfer
Replacement operator used
Control function determines when the transfer should take place

## Slide 7: 1. Bus transfer
Common bus system used
Multiplexers used to select source register whose information is placed on the bus
  Kx1 multiplexer if k registers are there
  No of select lines-log k
  For register of n bits, n multiplexers needed
Decoder selects the destination register
  Data transfer to destination takes place only if decoder enabled

## Slide 9: 2. Memory transfer
Read
Write

## Slide 11: Arithmetic microoperations

## Slide 13: Logic microoperations
Binary operations for a string of bits stored in registers
Each bit considered separately

## Slide 15: Shift microoperations
Shift accompanied with another microoperation- to specify value for extreme flipflop

## Slide 16: Conditional control statements
Equivalent :